## Slide 1
Methane emissions depending on manure management
Salvador Calvet Sanz
Institute of Animal Science and Technology
Universitat Politècnica de València
salcalsa@upvnet.upv.es
@SalvaCalvet

## Slide 2
Relevance of CH4
Emission mechanism
Excretion of manure
Potential emissions
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 4
https://www.bloomberg.com/graphics/2015-whats-warming-the-world/

## Slide 5
SF6
CO2
CH4
C2F4 (CFC)
N2O
…
Wide variety of GHG.
Greenhouse gases (GHG)

## Slide 6
https://www.eea.europa.eu/data-and-maps/data/data-viewers/greenhouse-gases-viewer
Gas | Emission (Tg/y) | % of total
CO2 | 3,489 | 79%
CH4 | 448 | 10%
N2O | 233 | 5%
Rest | 243 | 6%
Total amount of GHG (Europe)

## Slide 7
https://www.eea.europa.eu/data-and-maps/data/data-viewers/greenhouse-gases-viewer
Sector | CH4 (Tg/y) | % of total
Energy | 85 | 19%
Industry | 2 | 0.4%
Agriculture | 237 | 52%
Land use | 6 | 1.2%
Waste | 124 | 27%
CH4 by sector

## Slide 8
https://www.eea.europa.eu/data-and-maps/data/data-viewers/greenhouse-gases-viewer
Sector | CH4 (Tg/y) | % of Agriculture
Enteric fermentation | 191 | 81%
Manure | 41 | 17%
Agriculture | 2.6 | 1.1%
Land use | 0.6 | 0.3%
Waste | 1.4 | 0.6%
CH4 by sector
Manure ~ 1% of EU GHG

## Slide 9
 | Relative Warming Potential | Lifetime (years)
CO2 | 1 | 5-200
CH4 | 21 | 12
N2O | 298 | 114
HFC-134 | 1.300 | 13,8
Global Warming Potential

## Slide 10
The Horizon

## Slide 11
The role of non-CO2 emissions.
The Horizon
http://www.ipcc.ch/report/sr15/

## Slide 12
Relevance of CH4
Emission mechanism
Excretion of manure
Potential emissions
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 13
Manure management
Enteric fermentation
Methane (CH4)

## Slide 14
Organic matter
CH4
CO2
O2
Origin of CH4

## Slide 15
Mechanism
Carbohydrates, Proteins, Lipids
Sugars, amino acids, fatty acids, alcohols
Volatile fatty acids, simple alcohols
Acetate
H2 + CO2
CH4 + CO2
hydrolysis
Acidogenesis
Acetogenesis
Homoacetogenesis
Methanogenesis
Primary fermentative bacteria (acidogens)
Secondary fermentative bacteria (acetogens)
Hydrogenothrophic methanogenic archaea
Aceticlastic methanogenic archaea
Organic matter
Absence of oxygen
No inhibitions
Time

## Slide 16
Origen de las emisiones
Enteric fermentation
Ym = % of Energy intake emitted as CH4
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines

## Slide 17
Origen de las emisiones
Manure management
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines
VS excretion
(kg/animal/yr)
B0 = BMP (m3 CH4/kg VS)
Biochem. CH4 Potential
MCF (%)
CH4 conversion factor
CH4 (kg/yr) = VS x B0 x MCF x 0.67 kg/m3

## Slide 18
Relevance of CH4
Emission mechanism
Excretion of manure (VS)
Potential emissions (B0)
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 19
Origen de las emisiones
Energy balance at animal level
Gross energy
Digestible energy
Metabolizable energy
Net Energy
Faeces (Organic Matter = Volatile Solids)
Urine, enteric CH4
Heat
Nutrient balances

## Slide 20
Energy balance at animal level (research)
Antezana et al., 2018
MJ EB/kg LW increase

## Slide 21
Origen de las emisiones
Energy balance at animal level (inventory)
Animal Category | VS (kg/place/yr)
Piglets (6-20 kg) | 43
Fatteners (20-49 kg) | 131
Fatteners (50-79 kg) | 161
Fatteners (80-109 kg) | 180
Fatteners (> 110kg) | 204
Boars | 249
Pregnant sow | 229
Farrowing sows | 414
Depend on:
- Type of feed
- Type of animal
- Management

## Slide 22
Origen de las emisiones
IPCC default values for VS excretion
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines

## Slide 23
Origen de las emisiones
IPCC default values for VS excretion
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines

## Slide 24
Origen de las emisiones
IPCC default values for VS excretion
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines

## Slide 25
Relevance of CH4
Emission mechanism
Excretion of manure (VS)
Potential emissions (B0)
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 26
Origen de las emisiones
Biochemical Methane Production (BMP, B0)
“a laboratory batch digestion of the substrate in the presence of an anaerobic inoculum, at a certain inoculum to substrate ratio” (from Angelidaki et al., 2009).

## Slide 27
Origen de las emisiones
Biochemical Methane Production (BMP, B0)
Antezana et al., 2015

## Slide 28
Origen de las emisiones
Prediction of BMP (from composition)
Chemical Oxygen Demand (COD)
Elemental composition
(C, O, H, N)
Organic fraction composition
NIRS (Near Infra Red Spectroscopy)
Nielfa et al., 2015; Ward, 2016

## Slide 29
Origen de las emisiones
Prediction of BMP (from kinetics)

## Slide 30
Origen de las emisiones
Prediction of BMP (from composition)

## Slide 31
Relevance of CH4
Emission mechanism
Excretion of manure (VS)
Potential emissions (B0)
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 32
Origen de las emisiones
MCF values depending on many factors
• Timing of storage/application;
• Feed and animal characteristics
• Length of storage
• Manure characteristics
• Amount of manure left (inoculum);
• Temperature distribution (spatial, time)
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines

## Slide 33
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines
MCF by temperature and management

## Slide 34
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines
MCF by temperature and management

## Slide 35
https://www.ipcc-nggip.iges.or.jp/public/2006gl
IPCC Guidelines
MCF by temperature and management

## Slide 36
Calvet et al., 2017
Example: effect of aeration
Pig farm
Fattening pigs
6 m3 slurry
6 tanks, 1m3 each
3 control
3 aeration

## Slide 37
Calvet et al., 2017
Example: effect of aeration
Aeration
2 minutes every 6h
(3, 9, 15, 21h), 10 m3/h

## Slide 38
Calvet et al., 2017
Example: effect of aeration
Phase 1
No aeration
Phase 2
Aeration
Phase 3
No aeration

## Slide 39
Calvet et al., 2017
Example: effect of aeration
Log scale!
Aeration
2 minutes
Log scale!

## Slide 40
Relevance of CH4
Emission mechanism
Excretion of manure (VS)
Potential emissions (B0)
Methane conversion factor (MCF)
Summary
  Topics for today

## Slide 41
Origen de las emisiones
Calculated manure from pig slurry
VS excretion ~ 160 kg/place/year
B0 ~ 300 L CH4 / kg VS
MCF ~ 0 (solid manures)
>50% (slurries)
Depending on temperature
Up to ~ 7 kg CH4 per m3 of slurry
About ~200 kg CO2 eq per fattener produced

## Slide 42
Origen de las emisiones
Modelling perspectives
VS Excretion: Accurate with nutrition balances
BMP: Convenience for measured values
Can be estimated
MCF: Large variations
Factors critically affecting (T, management…)
More information needed

## Slide 43
Methane emissions depending on manure management
Salvador Calvet Sanz
Institute of Animal Science and Technology
Universitat Politècnica de València
salcalsa@upvnet.upv.es
@SalvaCalvet