## Slide 1
Development of ventilation based strategies to reduce ammonia & odour
emissions from pig fattening houses:
an integrated approach
Raphael Tabase, Jan Vierendeels, Eva Brusselman, Bart Sonck,
Peter Demeyer
COST LivAge Training School on modelling emissions
2019 March 16th
Notes: Objectives: Techniques and Management Tools for Pollutant Emission Reduction in Flemish Piggery

## Slide 2
EU regulations + odour abatement
Existing ‘expensive’ emission reduction systems (50-70%)
Need for additional low cost (management) systems (10-20%)
Hypothesis: lower ventilation rates ≈ lower emissions
Lower velocities near emitting surfaces
Prohibit displacement of pit headspace air
Integrated approach for detailed information
Measuring & modelling
Test platform & full scale experiments
Why?

## Slide 3: Ventilation settings
ΔTc = 5 °C
Vmax = 70 m3h-1pig-1
Vmin = 14 m3h-1pig-1

## Slide 4
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiments
Innovative Ventilation Regimes/Strategies

## Slide 5: Test object
ILVO-UGent
Pig Campus

## Slide 6
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 7: Indoor Climate Model
Time-dependent mass and energy balance equations
Validation with ILVO-UGent farm data
Reference ventilation regime & 9 others
Output MatLab
  Ventilation rate
  Indoor temperature & RH
  CO2
Strategies with higher CO2 concentrations (winter) removed
Strategies with lower average ventilation rates selected

## Slide 8
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 9: CFD Model
Spatial distribution of indoor T and air velocity near emitting surfaces
Assess different building design parameters on indoor air distribution
Compartment
32-48 pigs at 60 kg
Boundary conditions
From indoor climate model
Slatted floor as porous medium

## Slide 10: Validation with mock-up pigs

## Slide 11: Velocity Distribution
Pen 7
Pen 3
Pen 1
Walking alley
Notes: Below is plane in the middle of the ground channel
Winter conditions

## Slide 12
T_GC = 10 °C and VR = 714 m3 h-1
T_GC = 20 °C and VR = 1937 m3 h-1
Notes: Top graph showes air going into the pit (low GC T and VR)

## Slide 13
Inlet close to slurry pit and airflow by displacement

## Slide 14
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 15
CFD Model: NH3 Emission UDF for air volume source
UDF cell zone: extract velocity & T as mass transfer coefficient input parameters
Mass transfer Coefficient
(Haslam et al., 1924)
Notes: Air volume source

## Slide 16: Validation with real pigs
Temperature
NH3 (detection tube)
NH3 & CO2 measured at exhaust (FTIR)
48 pigs at ~90 kg

## Slide 17: Results
Parameter | Experiment | CFD
Room temperature (°C) | 23.2 ± 0.1 | 23.3
Exhaust CO2 (ppm) | 2138 ± 169 | 1981
Exhaust NH3 (ppm) | 16.1 ± 0.9 | 16.2
CO2 emission rate (g h-1) | 107.9 ± 9.5 | 98
NH3 emission rate (g h-1) | 0.40 ± 0.03 | 0.40
Notes: Room T is measured at 1,4m above slatted floor pen 3

## Slide 18: NH3 Distribution
Pen 7
Pen 3
Pen 1
Walking alley

## Slide 19
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 20: Test platform
Urea solution: 0.2 mol L-1
Temperature: 37 °C
Spray frequency: 3 u; 12 L; 0.99 L min-1
2.3 kW from mock-up pigs

## Slide 21
Set-point temperature | Vmin (m3h-1pig-1) | Vmax (m3h-1pig-1)
Tset = 23 °C (Control) | 14 | 70
Tset = 25 °C (T1) | 14 | 70
Tset = 21 °C (T4) | 14 | 70
Notes: Increase setpoint less emissions

## Slide 22
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 23: Full-scale Experiment
4 ventilation (C, T1, T2, T3) regimes in fully-slatted compartments
3 fattening rounds (August 2016 – November 2017)
Duplicate treatments per round (8 compartments)
NH3, CO2, CH4, N2O (FTIR)
Odour concentrations
Monitored pig performance
Control setpoint +2°C

## Slide 24
Indoor Climate Model
Promising ventilation strategies
CFD Model
Temperature &
Velocity distribution
NH3 Emission Model
Predict NH3 emission
Test Platform
Confirm ventilation strategies
Full Scale Experiment
Innovative Ventilation regimes/Strategies

## Slide 25: Full-scale Experiment
Variable | T1 | Control
Tout (°C) | 13.3 ± 5.7 | 13.3 ± 5.7
TGC (°C) | 15.1 ± 3.8 | 15.1 ± 3.8
Ti (°C) | 25.1 ± 1.1 (1.1) | 24.0 ± 1.2
VR (m3 h-1 pig-1) | 26.5 ± 10.3 (-26%) | 35.8 ± 11.9
NH3 Conc. (ppm) | 16.6 ± 4.1 (19%) | 13.9 ± 5.0
Odour Conc. (OUE m-3) | 1640 ± 481 (12%) | 1470 ± 633
NH3 ER (kg pig-1 yr-1) | 2.26 ± 0.70 (-11%) | 2.53 ± 0.87
Odour ER (OUE s-1 pig-1) | 11.3 ± 4.5 (-23%) | 14.7 ± 8.8

## Slide 26: Full-scale Experiment

## Slide 27
Thank you
Institute for Agricultural
and Fisheries Research
Burg. Van Gansberghelaan 115 box 1
9820 Merelbeke – Belgium
T + 32 (0)9 272 28 00
F +32 (0)9 272 28 01
t&v@ilvo.vlaanderen.be
www.ilvo.vlaanderen.be